## Slide 1: Stormwater Management: TCNJ Townhouses South
Kelly Hommen
Elizabeth Lafferty
Michael Murphy
Charles Stewart
Advisors: Dr. Michael Horst and Dr. Vedrana Krstic
1

## Slide 2: Introduction
26 individual units
  20 have noticeable moisture
  15 have standing water
Main concerns
  Termite damage
  Mold
Is this a runoff or an infiltration problem?
2

## Slide 3: Site Location
3

## Slide 4: Photos
4

## Slide 5: Problem Statement
How can the presence of moisture be significantly reduced from the crawlspaces to minimize the likelihood of termites and mold?
5

## Slide 6: Solution
Conduct hydrologic and soil analysis on the area in question to determine the properties of the watershed
Apply the data to determine total losses for given design storms
  Computer Modeling (HEC-HMS)
Develop a cost effective solution to remediate the problem previously stated
6

## Slide 7: Soil Analysis
Performed By:
Kelly Hommen & Elizabeth Lafferty
7

## Slide 8: Soil Analysis
Augured two test holes
  Collected soil samples 8.5 ft in depth
Conducted percolation tests in two locations
Installed a well for groundwater
table monitoring
8

## Slide 9
Percolation Test 1
Monitoring Well / Boring Sample 2
Boring Sample 1
Percolation Test 2
Test Locations
9

## Slide 10: Soil Tests
Moisture Content (ASTM D-2216)
Sieve Analysis (ASTM D-422)
  Grain Size Distribution Curves
Atterberg Limits (ASTM D-4318)
  Liquid Limit
  Plastic Limit
Percolation Testing (NJBMP Manual)
  Permeability
Burmister Soil Identification Method
10

## Slide 11: Soil Profile
11

## Slide 12: Permeability
Percolation Test conducted in two locations
  Represents the top 5 feet of soil profile
Permeability ≈ 0.001323
ft/min
Consistent with Das values for Fine Sand
with Silt
12
Notes: Compare to soil profile findings of silty sand

## Slide 13: Ground Water Well
13
Ground water monitoring indicated level was below 7’
Notes: GWT monitoring revealed no presence of water…GWT greater than 7 ft

## Slide 14: Soil Analysis Conclusion
Soil profile created
  Properties confirmed through soil testing
Hydraulic conductivity consistent with fine Sand, trace Silt
i-MAP NJ (DEP) – Confirmed area of interest not a wetland
Low groundwater table provides for the potential use of detention and retention basins
14
Notes: No significant design challenges involving soil/soil properties…infiltration problems with silty sand

## Slide 15: Hydrologic Analysis
Performed By:
Michael Murphy & Charles Stewart
15

## Slide 16: Watershed Delineation
Watershed Area: 83,736 sq. ft. = 1.92 acres
  Impervious Area: 42,723 sq. ft. = 0.98 acres
  Pervious Area: 41,013 sq. ft. = 0.94 acres
16

## Slide 17: Watershed Delineation
Longest hydraulic length
  Impervious: 645 ft
  Pervious: 735 ft
Slope: S=Δel/LHL
  Impervious S=3.89%
  Pervious S=3.41%
17

## Slide 18: Curve Number
Impervious
  CN = 98 (for impervious areas, paved parking lots etc.)
    Table 7.10 Runoff Curve Numbers for Urban Areas
    Introduction to Hydrology, 5th Edition
Pervious
  CN = 69 (for open lawn, fair condition, soil group B)
    USGS WebSoil Survey
    MbpB: Metapeake Loam
      Soil group B
18

## Slide 19: SCS Regression Method
SCS Regression Method used to determine lag times for later use in HEC-HMS
Tlag = (LHL0.8*(S+1)0.7)/(1900*Savg0.5)
  S=1000/CN – 10
Tlag pervious = 0.184 hours = 11.06 minutes
Tlag impervious = 0.054 hours = 3.22 minutes
19

## Slide 20: Computer Modeling
HEC-HMS
20

## Slide 21: Setup
HEC-HMS was used to determine the peak outflow and total losses affecting the area.
Sub-basins were created for each watershed
  Sub-basin 1 – Impervious
  Sub-basin 2- Pervious
Junction was created to connect the two sub-basins
Volume of total losses represents water infiltration that can contribute to flooding in crawlspaces
21
Notes: Inputs included CN, area, and lag times for each subbasin

## Slide 22: Input
Precipitation Depths were entered for a 2-yr Design Storm for 1, 2, 3, 6, 12, and 24 hours (NOAA’s National Weather Service)
Intensity: 1 hour
Duration: 1 day
22

## Slide 23: Impervious Results
23

## Slide 24: Pervious Results
24

## Slide 25: Junction Results
25

## Slide 26: Final Results
Total Losses: 2.59 inches
  Impervious: 0.12 inches
  Pervious: 2.47 inches
Total Infiltration
  83,736 ft2 * 2.59 in * (1 ft / 12 in) = 18,073 ft3
Future designs will be based on infiltration values.
26

## Slide 27: Proposed Solution #1
Re-grading of the Soil
  Soil in certain areas lies above the sill plate
  Allows water to enter through the porous material into the crawl space
27
Sill Plate

## Slide 28: Proposed Solution #2
Design and Install Sump Pumps
The units are divided by concrete block foundation walls
  Flooding is contained within each unit
  When the units were constructed, pre-formed pits were installed in each of the crawl space floors
Design a pump to remove standing water
28

## Slide 29: Proposed Solution #3
Roof Water Collection System
Design basin to collect roof water
  Reused within the Townhouses
  Discharged away from the area
29

## Slide 30: Budget
Estimated Cost for Fall Semester - $240.00
  Groundwater Measurement Device - $220.00
  Topographic Maps - $10.00
  PVC Pipe - $10.00
Full Cost Estimate to be provided in Senior Project II
30

## Slide 31: Gantt Chart
31

## Slide 32: Conclusion
Soil and hydrologic analyses indicate infiltration as the main cause of the accumulation of water in the crawlspaces
Senior Project II will consist of designing solutions to alleviate this problem
32

## Slide 33: Questions / Comments?
33